## Slide 1
ACL
Pivot point
Real-Time Rotational Torque Detection & Haptic Warning System
TEAM MEMBERS
Harshil Mishra
Shreesh Tripathi
Bhargavi Deo
Nandan Krishna S
Kamalnath
Intra Prodex
Notes: 1

## Slide 2
PROBLEM STATEMENT
Why are athletes still getting injured despite wearing braces?
How ACL Injuries Happen
  Knee twists too fast during landing or pivoting
  Tibial internal rotation exceeds safe threshold
  Ligament absorbs full torque - then snaps
  Non-contact injuries are most common (70%+)
The Critical Gap
  No real-time warning before ligament snaps
  Twist angle is invisible to the naked eye
  Traditional braces are purely passive
  No field-ready monitoring solution exists
The Data
  ₹3–8 Lakh surgery + 9–12 months recovery
  High recurrence: 15–25% re-injury rate
  Athletes in football, basketball, badminton most at risk
  68.6 ACL tears per 100,000 population in India
Current Braces Are Blind
  Resist forward movement, not hidden rotation
  No sensors to detect rotational torque
  Cannot trigger any warning in real-time
Notes: 2

## Slide 3
RESEARCH & LITERATURE REVIEW
The scientific foundation of our solution
01
Mechanism of Non-Contact ACL Injuries
PMC · 2022
ACL ruptures predominantly occur through tibial internal rotation combined with knee valgus - NOT direct contact. Landing/pivoting biomechanics are the primary culprit.
Insight: Rotation is the root cause.
02
Tibial Internal Rotation & ACL Strain
PMC · 2024
Excessive tibial internal rotation beyond 15°-20° significantly increases ACL loading. This threshold is measurable via differential IMU readings across the joint.
Insight: Gives us our exact Red Zone threshold (15°–20°) for haptic alerts.
03
Knee Flexion Angles & ACL Injury Risk
medRxiv · 2025
ACL injuries peak at low knee flexion angles (< 30°). Athletes land stiff-legged during fatigue, increasing rotational risk. Real-time feedback can correct this.
Insight: Validates need for in-field, real-time monitoring rather than lab analysis.
04
Design of Real-Time ACL Monitoring System
ResearchGate · 2024
IMU-based systems using ESP32 can achieve sub-100ms response latency for joint angle calculations. Differential processing between two sensors is validated as accurate.
Insight: Confirms our ESP32 + dual MPU-6050 architecture is technically feasible.
Notes: 3

## Slide 4
EXISTING SOLUTIONS & THEIR GAPS
Every current solution fails athletes
Solution
What It Does
Critical Limitation
Conclusion
DonJoy / Breg
Functional Braces
Rigid mechanical frame; limits extreme flexion & extension
100% passive - zero sensor data, cannot detect or warn about hidden rotational torque
Blind to rotation
Vicon Optical
Motion Capture
Sub-millimeter 3D tracking of all joint kinematics via camera arrays
Requires lab setup with multiple cameras. Completely unusable on sports fields or clinics
Lab-only, costs lakhs
Smart Compression
Sleeves (e.g. Athos)
Track general metrics (steps, jump height) via embedded single sensors
No rigid support frame - cannot absorb torque. No differential angle processing or haptic alert
No rigid support, no haptics
Our Dynamic
Knee Ankle Support
Dual IMU + rigid frame + real-time differential processing + haptic biofeedback
Currently requires per-athlete calibration.
Field-ready, real-time, way less cost than our competitors
No existing solution combines mechanical support + real-time sensing + haptic alert in a field-deployable, affordable package.
Notes: 4

## Slide 5
OUR SOLUTION - SYSTEM OVERVIEW
A two-part system: physical protection with technological integration
PART 1 - MECHANICAL FRAME
1
Dual Cuff Frame
Tapered thigh + calf cuffs for secure fit
2
Aluminum Rods
Lateral rigid rods absorb rotational torque
3
Revolute Hinge
Lap-joint pin mirrors knee's natural rotation axis
4
Sliding Slot
Calf rod slot allows free bending, resists twist
5
Strap System
D-Ring Velcro locks frame to bone movement
+
PART 2 - IoT MONITORING BRAIN
1
Dual MPU-6050 IMU Array
One sensor on thigh, one on calf
2
ESP32 Controller
Pulls data from both IMUs, calculates parameters
3
Differential Processing
Based on Thigh rotation & Calf rotation
4
Haptic Alert
ERM motor fires when angle > Red Zone
5
Bluetooth Logging
Streams movement data to smartphone/coach app
Notes: 5

## Slide 6
MECHANICAL DESIGN
External skeleton engineered to protect without restricting natural athletic movement
Dual Tapered Cuff Frame
Two cuffs (Thigh & Calf) shaped wider at top, narrower at base - mirroring leg anatomy for anti-slip fit. Prevents the brace from sliding during dynamic movement.
Lateral Aluminum Rods
Rigid rods mounted on the lateral (outer) side. Thigh rod fixed via two bolts for a solid femoral anchor. Calf rod secured through a sliding oval slot.
Revolute Hinge (Lap Joint)
Two rods joined at the knee via a lapped pin joint, mimicking the knee's primary flexion axis. Metal stiffness resists the twisting forces that cause ACL tears.
Kinematic Sliding Slot
The calf rod's bolt sits in a vertical oval slot - allows free knee bending (flexion) while maintaining constant lateral and rotational guidance of the lower leg.
D-Ring Velcro Strap System
Loop-back Velcro straps threaded through integrated D-ring slots. Creates high-pressure compression lock ensuring sensors stay perfectly synced with bone movement.
Notes: 6

## Slide 7
IOT & SENSING ARCHITECTURE
How the system reads, processes, and reacts to dangerous rotation in milliseconds
MPU-6050 (Thigh)
I2C Address: 0x68
Tracks femur orientation via 6-axis gyro+accel
▶
MPU-6050 (Calf)
I2C Address: 0x69
AD0 pin bridged HIGH to offset address
▶
ESP32 Controller
Pulls data from both IMUs via I2C bus
High-frequency real-time processing
▶
Differential Processing
Twist Angle = Calf Yaw − Thigh Yaw
Calculated every sensor cycle
▶
Haptic Output
Digital signal to ERM motor
Alert fires if angle > Red Zone
AD0 Address Trick
Two identical MPU-6050 chips share one I2C bus. The calf sensor's AD0 pin is wired HIGH, shifting its I2C address from 0x68 → 0x69 to avoid collision.
Differential Formula
Twist Angle (°) = Thigh Gyro Yaw − Calf Gyro Yaw
This net rotation isolates the knee's internal/external rotation irrespective of whole-body movement.
Bluetooth Data Logging
ESP32's onboard BLE module streams timestamped angle data to a smartphone. Movement patterns are logged for post-session coach/doctor review.
Notes: 7

## Slide 8
HAPTIC FEEDBACK LOOP
From dangerous angle to corrective warning
SAFE ZONE (0°–15°)
WARNING (15°–20°)
RED ZONE (>20°) - ALERT FIRES
01
Athlete Pivots
During a landing or cut, the knee begins rotating. Both MPU-6050 sensors capture real-time orientation data independently.
→
02
ESP32 Calculates Twist Angle
The controller subtracts calf yaw from thigh yaw to compute the exact internal rotation of the knee joint in real time.
→
03
Red Zone Threshold Crossed
If the differential angle exceeds 15°-20°, the ESP32 identifies a high-risk event. A trigger signal is generated.
→
04
ERM Motor Fires
The embedded Eccentric Rotating Mass vibration motor activates, delivering a sharp tactile pulse directly against the athlete's skin.
→
05
Athlete Self-Corrects
The physical sensation is an instant reflex trigger. The athlete adjusts stance or landing mechanics before reaching ligament failure threshold.
Vibration alert is instantaneous; the athlete feels it before the ligament reaches its mechanical failure point.
Notes: 8

## Slide 9
KEY FEATURES SUMMARY
6 integrated features that set the Dynamic Knee Ankle Support apart
Kinematic Sliding Slot
Oval slot on calf rod, free bending, constant rotational resistance
Dual-Node IMU Array
Two MPU-6050s track femur vs. tibia orientation independently
Real-Time ESP32 Processing
High-frequency on-device computation
Haptic Biofeedback Alert
Instant tactile pulse when knee enters dangerous Red Zone
Load-Sharing Mitigation
Rigid frame absorbs mechanical stress alongside the ligament
Bluetooth Data Logging
Streams movement patterns wirelessly to coach/doctor app
Notes: 9

## Slide 10
COST ANALYSIS
A ₹1,950 solution vs. alternatives
Category
Component
Cost
Microcontroller & Sensors
ESP32 + 2× MPU-6050 IMU
₹800
Haptic Feedback
ERM Vibration Motor + Driver
₹150
Power Supply
3.3V Li-ion Battery + Switch
₹100
Wearable Base
Compression Knee Sleeve
₹450
3D Printed Frame
PETG / Nylon / CF-PLA Filament
₹300
Mechanical Fasteners
M4 Shoulder Bolts + Nyloc Nuts
₹150
Wiring & Misc
Jumper Wires, connectors
₹0
TOTAL ESTIMATED COST
~₹1,950
Cost Comparison vs. Alternatives
Vicon Motion Capture
₹20–50 Lakh
DonJoy Brace
₹5,000–15,000
Smart Sleeves
₹3,000–8,000
Our Solution
₹1,950
At ₹1,950, our device is 2.5–8× cheaper than passive-only braces, and over 1,000× cheaper than lab systems.
Notes: 10

## Slide 11
TARGET MARKET
A multi-tier addressable market from grassroots sports to professional rehabilitation
PRIMARY MARKET
Athletes — College & Professional
Channels:
Football • Basketball • Badminton • Volleyball • Wrestling
Why they need us:
High-ACL-risk sports with frequent pivot, cut, and landing movements. First adopters who directly benefit from real-time injury prevention.
68.6 ACL tears per 100,000 population
SECONDARY MARKET
Post-Surgical Rehab Patients
Channels:
Physiotherapy clinics • Orthopaedic hospitals • Sports medicine centres
Why they need us:
Recovering athletes need biomechanical monitoring to avoid re-injury. Our device provides data-driven rehab with haptic correction for safe return-to-sport.
15–25% re-injury rate post-ACL reconstruction
TERTIARY MARKET
Institutions & Training Bodies
Channels:
Sports academies
School/college sports programs
Why they need us:
Institutional procurement for injury prevention monitoring across squads. Coach dashboards and data analytics create ongoing subscription value.
Global sports medicine market: $9.2B (2024)
Global sports medicine market projected to reach $15.3B by 2030 — growing at 6.5% CAGR (Grand View Research)
Notes: 11

## Slide 12
RISKS & LIMITATIONS
Transparent risk assessment - and our mitigation roadmap for each
Sensor Drift Over Time
Risk:
Gyroscope bias accumulates → angle readings become inaccurate after extended use.
Mitigation:
Periodic re-calibration protocol + drift-correction algorithm in firmware.
Comfort
Risk:
Rigid frame may cause discomfort in long matches; athletes may remove brace.
Mitigation:
Comfortable padding, lightweight materials, comfort-testing iterations.
Per-Athlete Calibration
Risk:
Each user requires individual calibration for accurate Red Zone thresholds.
Mitigation:
Auto-calibration routine on first use; ML-based adaptive baseline.
Not a Medical Replacement
Risk:
Device is a warning system — cannot prevent all injuries or replace clinical assessment.
Mitigation:
Clear usage guidelines + medical professional integration in dashboard.
Regulatory Pathway
Risk:
Medical device clearance required before clinical or commercial deployment.
Mitigation:
Plan: Start as sports training aid
Battery Life Constraints
Risk:
3.3V Li-ion battery limits continuous operation — replacement/recharging during matches.
Mitigation:
Low-power ESP32 sleep modes; wireless charging coil integration planned.
Notes: 12

## Slide 13
FUTURE PROSPECTS
The roadmap from prototype to AI-powered sports safety platform
ML & Predictive Analytics
Leveraging Bluetooth-logged biomechanical data, machine learning models will learn each athlete's unique movement patterns and establish personalized baselines. The system will predict fatigue-related injury risk BEFORE kinematics enter the danger zone.
ML on ESP32
Anomaly detection
Long-term pattern learning
Personalized Fatigue-Risk Baselines
Each athlete's 'normal' rotation profile varies. Adaptive calibration will auto-adjust Red Zone thresholds based on individual biomechanics, sport type, and real-time fatigue levels detected from gait pattern degradation.
Adaptive thresholds
Fatigue modelling
Sport-specific profiles
Miniaturisation & Wireless Charging
Replacing current components with miniaturized alternatives and integrating a wireless charging coil will reduce device weight by 40%+. Form factor will shrink to a discreet sensor patch worn beneath athletic gear.
miniaturization
wireless charging
Sub weight
Coach & Doctor Dashboard App
A cross-platform mobile/web app providing coaches and physiotherapists with real-time biomechanical dashboards, session reports, injury risk heatmaps, and long-term trend analysis for entire squads.
App
Squad analytics
Injury risk heatmaps
Notes: 13

## Slide 14
THANK YOU

## Slide 15
APPENDIX - Circuit Diagram & Visual representation
Notes: 14

## Slide 16
APPENDIX – CAD & References
Mechanism of non contact ACL injuries
PMC · 2022
Tibial internal rotation
PMC · 2024
Relation of Kneeflexion angles with ACL injuries
medRxiv · 2025
Design and Development of a Real-time Monitoring System for ACL Injury Prevention
ResearchGate · 2024
ESP32 programming guide
Notes: 15